ITD Workspace Installation Process for Consultants

# Section 1 – Server Setup

The following process is required to properly install and use the ITD workspace.  This workspace is very customized and specific to the processes at ITD.  However, this workspace has been designed understanding that you have a need to use MicroStation and InRoads without the ITD workspace and thus does not take over your MicroStation installation.  You will be able to easily start either the ITD workspace or the default MicroStation workspace by selecting a different icon.

The following actions should be completed on a file server that is accessible by everyone in your organization that will use the ITD workspace.  If you do not have a network or are setting the ITD workspace up on a single computer, please review Appendix A before continuing.

Setup Server folders

- Create an empty folder that will store the ITD Projects Files.

- Share the folder created for the ITD Projects Files.  Make certain that users have read/write access to this share.  
This folder should be mapped to the P: drive on the local machines.

- Extract the ITD_Workspace.zip file to the file server.  This zip file will create a new folder named ITD_Workspace that will contain all of the necessary files for the ITD workspace.

- Share the ITD_Workspace folder.  Make certain that users have read/write access to this share.  
This folder must be mapped to the S: drive on the local machines.  
This is important because there are several areas within the MicroStation and InRoads workspace that look for the S: drive mapping and these portions of the software cannot be mapped using a more flexible URL scheme at this time.

Each user working in the ITD Workspace must have unique resource files for their personal environment.  These files include AccuDraw short cuts, Function Key menus, MicroStation Interface, User Preference File, and DWG translation definitions.

- Run the batch file S:\User_Workspace\Create Users.bat

- When prompted, enter the Windows login for the person who will be logged in when running MicroStation and InRoads with the ITD Workspace.  The appropriate folders and files for the new user are created in the S:\User_Workspace\Users\ folder.

- Repeat this process for each user who will be working in the ITD Workspace.

# Section 2 – Local Workstation Setup

The following process is required to properly install and use the ITD workspace.

Map network drives

- Share the folder created for the ITD Workspace.  This folder must be mapped to the S: drive on the local machines.  
This is important because there are several areas within the MicroStation and InRoads workspace that look for the S: drive mapping and these portions of the software cannot be mapped using a more flexible URL scheme at this time.

- Share the folder created for the ITD Projects Files.  This folder should be mapped to the P: drive on the local machines.

Software

- Power InRoads.  As of the date this document was published, ITD is using version 08.11.09.845.  Please check with ITD to verify if this is the correct version.

After the software is installed, it must be configured to work with the ITD Workspace.

- Copy the file S:\Software\Local_CFG_File\ITD_Standards_Local.cfg to the folder C:\Program Files\Bentley\MicroStation\config\appl\ or equivalent folder if MicroStation was installed to a different drive or folder.
This configuration file facilitates MicroStation to use the ITD Workspace.  However, it does not automatically enable the ITD Workspace.  To enable the ITD Workspace you must also complete the following steps.

- Create a copy of the Power InRoads icon and label it ITD Power InRoads.

- Right-click on the new icon and select Properties. Add the switch –ws ITD USER=1 to the target on the shortcut tab as illustrated in the following example:
    "C:\Program Files\Bentley\MicroStation\ustation.exe" -ws_ITD_USER=1
     *Note - Your path to MicroStation may vary based upon your installation location.

- Use this icon to start MicroStation or InRoads using the ITD workspace.  Using the original MicroStation icon, the Start menu, or double clicking on a DGN file will start MicroStation without the ITD workspace.

- Copy the Quantity Manager configuration file S:\Software\Local_CFG_File\qm.cfg to the folder C:\Program Files\Bentley\InRoads Group V8.9\QM\classes| or equivalent folder if InRoads was installed to a different drive or folder.

# Appendix A – Working without a File Server

If you are installing the ITD Workspace on a single computer and not using a client-server configuration you need to simulate the server environment.  If your computer does not have a network card or you are not currently connected you may need to use the Microsoft Loopback adapter.

The following instructions are for Windows XP and are taken from Microsoft KnowledgeBase article 839013.

To manually install the Microsoft Loopback adapter in Windows XP, follow these steps:

- Click Start, and then click Control Panel.

- If you are in Classic view, click Switch to Category View under Control Panel in the left pane.

- Double-click Printers and Other Hardware, and then click Next.

- Under See Also in the left pane, click Add Hardware and then click Next.

- Click Yes, I have already connected the hardware, and then click Next.

- At the bottom of the list, click Add a new hardware device, and then click Next.

- Click Install the hardware that I manfully select from a list, and then click Next.

- Click Network adapters, and then click Next.

- In the Manufacturer box, click Microsoft.

- In the Network Adapter box, click Microsoft Loopback Adapter, and then click Next.

- Click Finish.